## Slide 1
AERONAUTICAL INFORMATICS
Avio23
An IMA Teaching Platform
Where every partition has its turn.
apl. Prof. Dr.-Ing. Umut Durak
DLR Institute of Flight Systems · TU Clausthal

## Slide 2
01 — WHY IMA
Where avionics software runs today
Pre-IMA (federated)
One LRU per function. Dozens of boxes. Each owns its CPU, wiring, certification.
IMA (today)
A handful of shared CPMs hosting many partitions. Shared CPU, shared bus, isolated logic.
Modern cockpit software (A350, B787, E2, Global) runs the right column.
Avio23 · Aeronautical Informatics · DLR / TU Clausthal
2

## Slide 3
02 — WHAT IMA PROVIDES
Three properties certification depends on
01
Space partitioning
One partition cannot corrupt another partition's memory. Hardware-enforced isolation.
02
Time partitioning
One partition cannot steal another partition's CPU time. Static schedule, hard guarantees.
03
Deterministic schedule
Every partition runs at known times every frame. Timing analysable, hard real-time.
Avio23 · Aeronautical Informatics · DLR / TU Clausthal
3

## Slide 4
03 — STANDARD
ARINC 653 in one slide
Partition | An isolated application with its own memory and its own scheduled time slot.
Major frame | The repeating period (40 ms in Avio23) that contains one slot for every partition.
Time window | A partition's (offset, duration) inside the major frame.
Sampling port | One-way mailbox; latest-value semantics; no queue.
Queueing port | One-way FIFO; messages preserved in order.
Health monitor | Watchdog that escalates partition faults.
We use sampling ports today — perfect for periodic sensor data.
Avio23 · Aeronautical Informatics · DLR / TU Clausthal
4

## Slide 5
04 — ARCHITECTURE
Avio23 — 5 nodes, 14 partitions
sim_gateway
IOM · 172.20.0.2
CPM-L
Landing Gear
172.20.0.3
DAL B
CPM-F
Fuel
172.20.0.4
DAL C
CPM-A
ECS
172.20.0.5
DAL D
CPM-E
Electrical
172.20.0.6
DAL B
Each box is a Docker container running its own a653rs-linux hypervisor.
Boxes talk over a virtual AFDX network (UDP on a Docker bridge).
Avio23 · Aeronautical Informatics · DLR / TU Clausthal
5

## Slide 6
05 — SCHEDULE
Inside one CPM — the 40 ms major frame
gateway
3 ms
fuel_qty
2 ms
transfer_pump
2 ms
idle margin
33 ms
0ms
10ms
20ms
30ms
40ms
33 ms idle is intentional — headroom for the partition you will add.
Static, repeating, deterministic.
Every partition gets exactly one window per frame. Misses are catastrophic.
Avio23 · Aeronautical Informatics · DLR / TU Clausthal
6

## Slide 7
06 — INTER-PARTITION COMMS
Sampling ports across CPMs
sensor_partition
in CPM-X
cpm_x_gateway
AFDX TX
cpm_y_gateway
AFDX RX
consumer_part
in CPM-Y
sampling port
UDP over AFDX
sampling port
Inside a CPM: ports are shared memory. · Between CPMs: gateways serialize port content to UDP.
Application code is identical in both cases — that is the whole point.
Avio23 · Aeronautical Informatics · DLR / TU Clausthal
7

## Slide 8
07 — DOMAINS
Four domain CPMs and what they do
CPM | Domain | DAL | Function
CPM-L | Landing Gear | B | Gear lever, braking, steering
CPM-F | Fuel | C | Fuel quantity, transfer pumps, balance
CPM-A | ECS / Air Conditioning | D | Bleed air, cabin temperature
CPM-E | Electrical / Energy | B | Generators, load shedding
Today everyone works in CPM-F.
DAL C — fuel loss leads to engine starvation, not direct loss of aircraft.
Avio23 · Aeronautical Informatics · DLR / TU Clausthal
8

## Slide 9
08 — ZOOM: CPM-F
Four partitions on one Fuel CPM
cpm_f_gateway
to/from AFDX network
fuel_quantity
given (reference)
transfer_pump
given (reference)
fuel_controller
← YOU BUILD THIS
(spare slot)
—
You will configure its slot in cpm_f.yaml, then implement select_source_tank in controller.rs.
Avio23 · Aeronautical Informatics · DLR / TU Clausthal
9

## Slide 10
09 — LIVE DEMO
Avio23 running, right now
avio23 — bash
$ docker compose up -d
Creating sim_gateway, cpm_l_node, cpm_f_node, cpm_a_node, cpm_e_node
$ docker compose logs -f sim_gateway
[sim_gateway] tx tank_l=247.3L tank_r=247.1L flow=0.10L/s
[cpm_f] rx fuel_qty total=494.4L imbalance=0.2L
[cpm_f] controller selected source=Left, age_since_switch=2.4s
[sim_gateway] tx tank_l=247.0L tank_r=247.1L flow=0.10L/s ...
This is what your passing solution looks like by the end of the session.
10

## Slide 11
10 — WHY THIS COURSE
Why bother with IMA at all?
It's how real cockpits are written
The pattern in Avio23 is the pattern in every modern commercial cockpit.
Integration is the avionics skill
Allocating ports and slots is what distinguishes avionics from generic embedded.
You learn the standards' vocabulary
DO-297, ARP4754A, ARINC 653 — all written in the language you use today.
The hard part isn't the algorithm — it's the constraints around it.
Avio23 · Aeronautical Informatics · DLR / TU Clausthal
11

## Slide 12
11 — ASSIGNMENT
Today: Fuel Management System
Two deliverables. Both graded automatically.
PART 1
Configuration
Add a fuel_controller partition to cpm_f.yaml. Pick a time window. Wire the sampling ports for sensors in and actuators out.
File: cpm_f.yaml
~15 minutes
PART 2
Controller logic
Implement select_source_tank(left, right, current, secs_since_switch) → Tank. Keep |L−R| ≤ 10 L. Respect the 0.8 s valve cooldown.
File: src/controller.rs
~40 minutes
Avio23 · Aeronautical Informatics · DLR / TU Clausthal
12

## Slide 13
12 — CONSTRAINTS
What makes this interesting
10 L
BALANCE
Max tank imbalance under any flight condition
0.8 s
COOLDOWN
Min interval between pump-valve switches
40 ms
CYCLE
Major frame — controller is invoked every tick
The interesting bit:
the cooldown and the balance requirement are coupled. A naive "switch whenever imbalanced" controller violates the cooldown. You have to think about state.
Avio23 · Aeronautical Informatics · DLR / TU Clausthal
13

## Slide 14
13 — TOOLCHAIN
Your laptop, nothing else
1. Validate your config
$ cargo run --bin test_bench -- --validate-config
Catches missing partition entries, port mis-wiring, frame budget overruns.
2. Run a scenario
$ cargo run --bin test_bench
Replays a 600-s flight scenario; writes out/trace.csv for plotting.
3. Run the grader (= your grade)
$ cargo test --release -- --nocapture
Identical to what I'll run on your submission at the end of the session.
No Docker, no Linux VM, no AFDX setup on your laptop.
Pure Rust crate. cargo run, cargo test. That's it.
Avio23 · Aeronautical Informatics · DLR / TU Clausthal
14

## Slide 15
14 — SCHEDULE
Your next two hours
0:00 – 0:20
This intro
TUTOR
0:20 – 0:30
Assignment briefing
TUTOR
0:30 – 0:45
Part 1 — Configuration
YOU
0:45 – 1:25
Part 2 — Controller logic
YOU
1:25 – 1:50
Grading + live demo on the real stack
BOTH
1:50 – 2:00
Wrap-up, grades, leave
—
Questions?
Then let's go.
Avio23 · Aeronautical Informatics · DLR / TU Clausthal
15